Loop
Collect Sensor Input
Joystick
Pressed
 Create modifiers to Angle
to generate Movement
by controlled toppling
Yes
No
Calibrate Stable Angle
Make corrections using Wheels
Sample Code:
void loop()
{
collectSensorInput();
if ( joystickPressed() )
createMovementPatchAngle();
}
else
calibrateStableAngle();
correctUsingWheels();

---
Collect Sensor
input
Collect Joystick Forwards
Collect Joystick Left
Collect Sensor Angle
Collect X Acceleration
Return
void collectSensorInput()
/* Store the sensor input in a global struct */
joystickForwards = map(
analogRead(JOYSTICK_FORWARDS_PIN),
0, 255, -127, 128
);
joystickLeft = map(
analogRead(JOYSTICK_LEFT_PIN),
0, 255, -127, 128
);
…

---
Calibrate
Stable
angle
Note: 1A
Close to target
Stable Angle
X Acceleration
Is Zero
Low Pass Filter
X Acceleration
Add Modification to Stable Angle
void calibrateStableAngle()
if( abs(sensorAngle - targetStableAngle) < something) )
if(XAcceleration > something)
calibratedStableAngle += (XAcceleration * something);
Notes:
1A: If the Segway is moving towards a new target center, after the target center has been changed due to joystick event, we can not use this to calibrate the target position.

---
    Create
 Movement
Patch Angle
Low Pass Filter
Joystick Forwards
Set
Movement Angle Patch
To
Joystick Forwards
Low Pass Filter
Joystick Left
Set
Turning differential
To
Joystick Left
void moveTargetAngle()
if( abs(joystickForwards) > something )
movementAnglePatch = (joystickForwards * something);
if( abs(joystickLeft) > something) )
turningDifferencial = (joystickLeft * something);

---
Correct
using
Wheels
Calculate Wheel Speed
From difference between
Sensor angle and target
Add calibration angle and
Movement patch Angle
Close to target
Stable Angle
Angle is too
Big to correct
Add turning differencial
Apply to wheels
void correctUsingWheels()
if( abs(sensorAngle - targetAngle) < something)
if(abs(sensorAngle - targetAngle) > something)
/* Note the sign of the turning differencial */
applyToRightWheel(wheelSpeed() + turningDifferencial);
applyToLeftWheel(wheelSpeed() - turningDifferencial);
float wheelSpeed()
float targetAngle = calibratedStableAngle + movementAnglePatch;
Return (sensorAngle – targetAngle) * something

---
Global
Semaphores
Sensor Inputs
Joystick Forwards
Sensor Angle
Joystick Left
XAcceleration
Movement Angles and Adjustments
Calibrated Stable Angle
Turning differential
Turning differential
Turning differential
Movement Angle Patch